## Slide 1: ADP 151/20 Kolloquium
Betreuer: Cheng Wang, Kai Domhardt
Topic: Development and Implementation of a Planner for Intersection Scenario for Automated Vehicle

## Slide 2: Agenda
Motivation and Methodology
Framework
Behavior Planner – (Straight FSM)
Behavior Planner – (Intersection FSM)
Trajectory Planner
Evaluation
Outlook

## Slide 3: Motivation
Pivotal roles in autonomous vehicles
    Plan decision-making system
    Trajectory planning
Existing research
    Capable of simplified conditions
Complex traffic condition
    Nose-to-tail traffic
    Overtaking

## Slide 4: Methodologie
V Model
  System requirement
    Szenario complexity
    Safety, efficiency, comfort
  System Engineering
    Behavior planner
    Trajectory planner
  Component Design
    Finite state machine
    Collision check
    Cost function
    Trajectory generation
Product requirement
System engineering
Component
Design
Component
integration
System integration
Product integration
Component implementation
Verification
Verification
Verification

## Slide 5: Framework
Input
  Global Route
  Traffic sign
  Obstacle position & velocity
  Ego car position & velocity
Output
  Steering wheel angle
  Odometer velocity
  Direction indicator

## Slide 6: Behavior Planner – (Straight FSM)
State | Description
Buffer | Accepting command from upper layer and send information to trajectory planner
Keep Lane | Driving at the current lane, including acceleration and deceleration
Stop | Stop for collision
Prep Left/ Right | Computation of the possibility for turning right/left
Change Left/ Right | Change left/ right, set the Turn Left/ Right flags when successfully finished the turn preparation

## Slide 7: Behavior Planner – (Straight FSM)
Scenario-based design of FSM：
  Lane change strategy
Scene-based division of tasks：
  Data processing of surrounding vehicles
  Cost function for judgement of changing lane
  Prediction of distance for lane change
Implementation of methods:
  ::cost_function()  optimal route

## Slide 8: Behavior Planner – (Straight FSM)
Speed penalty
Different lane penalty
Distance penalty
 Cost function:

## Slide 9: Behavior Planner – (Straight FSM)
1. Ensure body length
2. Avoid collision

## Slide 10: Behavior Planner – (Intersection FSM)
Scenario-based design of FSM：
  Traffic light
  Stop sign
  “RvL” (Rechts vor Links)
Scene-based division of tasks：
  Interaction with ahead obstacles
  Prediction of transverse obstacles
  Communication with traffic lights/ signs
  Determination of motion target
Implementation of methods:
  ::collision_check()  safety
  ::area_recognition()  legality and efficiency
  ::motion_decision()  safety

## Slide 11: Behavior Planner – (Intersection FSM)
Collision boundary area
  Interaction with ahead obstacles
  Prediction of transverse obstacles

## Slide 12: Behavior Planner – (Intersection FSM)
Communication with traffic lights
  distance based area recognition
Area | Description | Response
A | Far away | keep driving, no response to traffic light.
B | Approaching intersection | brake, if traffic light is red or yellow (from green)
C | Crosswalk | brake, if traffic light is red.
D | Inside of intersection | keep driving, no response to traffic light.

## Slide 13: Behavior Planner – (Intersection FSM)
Determination of motion target
  Processing in vehicle coordinate
    Acceleration
    Velocity
    Position

## Slide 14: Trajectory Planning
Basic Workflow：
  Map parsing
  Trajectory generator
  Trajectory selection
Map Parsing:
  Set up global path manually
  Geometry feature extraction (line, arc and poly curve)
  Generating list of point from path in Planner required format
Test field in Griesheim with 3 crossroads

## Slide 15: Trajectory Planning
Trajectory Planner Design
  Map reading
  Coordinate transformation
  Trajectory generation
  Optimal trajectory selection
  Motion control

## Slide 16: Trajectory Planning
Frenet coordinate
  Arc length and lateral offset as the basic axis
  Two dimensions: Longitudinal and Lateral
  Simplifying calculation in trajectory generation
Transfer between Frenet and Cartesian
  Cartesian to Frenet：
    to
    Simplifying calculation
  Frenet to Cartesian ：
    to
    target state for motion controller in Cartesian

## Slide 17: Trajectory Planning
Lateral movement in Frenet coordinate
  Quintic-polynomial :
    Start state
    End State
    Time of action
Longitudinal movement in Frenet coordinate
  Quintic-polynomial :
    Start state
    End State
    Time of action
Combination of movements in two directions
  Output the trajectory with discrete points combined with and

## Slide 18: Trajectory Planning
Trajectory Selection
  Over 100 trajectory candidates
  Defined Criterium for selection
    Cost function (comfort, total time cost, displacement error)
    Safety check (Vehicle dynamics limitation and collision free)
Cost Function
    ,where is the integral value of jerk squared
    is lateral offset ; longitudinal movement
Safety check
  Maximum velocity, acceleration and curvature
  Collision free

## Slide 19: Trajectory planning
Motion control
  Lateral distance-based division of control model
    Small distance  P control on steering angle
    Middle distance  Lateral distance dominated control with large turning radius
    Large distance  Lateral distance dominated control with small turning radius

## Slide 20: Evaluation
Open loop test
  State transition
    Overtaking opportunity
    Traffic light reaction
    Avoid collision
  predicted motion target
Closed loop test
  Inverse TTC compare

## Slide 21: Evaluation – (Straight FSM)
Open loop test
  Overtaking maneuver (Prep Change lane left  Change Lane left)
  TTC1: time to the front obstacle
  TTC2: time to the left lane front obstacle
Conclusion:
  fail to change the lane left
  reach in the front of the left obstacle
  the ego car could cut in the “Gap”
TTC1(s) | TTC2(s) | PCL->LCL
17.5 | 22.32-27.36 | Failed
15.41 | 19.8-21.6 | Failed
13.71 | 18.48-19.92 | Failed

## Slide 22: Evaluation – (Intersection FSM)
Open loop test
  Traffic light scenario without traffic participants
    Correctness of state transition with traffic light

## Slide 23: Evaluation – (Intersection FSM)
Open loop test
  Traffic light scenario with traffic participants
    Correctness of state transition with obstacles

## Slide 24: Evaluation – (Intersection FSM)
Open loop test
  Traffic light scenario with traffic participants
    Correctness of predicted motion target
Relative longitudinal distance between obstacles and target in Frenet |  |  | 
mean | std | max | min
42.97 m | 50.26 m | 263.40 m | 0.31m

## Slide 25: Evaluation – (Intersection FSM)
Closed loop test
  Traffic light scenario with traffic participants
  iTTC results comparison (Planner vs. IPG CarMaker)
    Similar safety performance as IPG built-in algorithms

## Slide 26: Outlook
Behavior Planner
  Accurate prediction of obstacles collision
    Processing in Frenet coordinate system
    Obstacles motion prediction based on probability  neural network
  Global planning in top-level layer
    Multi-threaded real-time loading high-precision map information
    Re-planning ability
Trajectory Planner
  Selection of weight coefficients for cost functions
    Optimization problem & parameter fine tuning

## Slide 28: Back-up
series connection
parallel connection
Hybrid connection
Talos from Team MIT
Junior from Stanford University and Volkswagen
Odin from Team VictorTango
    + Clear logic
    + High accuracy on solving solutions
    - Easy to collapse
    - Extensibility
    + Adapt with complex scenario
    + Fast and flexible reaction
    - High computation load
    + Hierarchical structure and clear logic
    + Adapt with complex scenario
    + Fast and flexible reaction

## Slide 29: Back-up

## Slide 30: Back-up
condition | description
S1 | no collision && no right turn && no left turn
S2 | no collision && very close to stopline
S3 | no collision && far from the stop line && (last try success ¦¦ long from last failure) && (want to turn left ¦¦ cost function is true)
S4 | no collision && far from the stop line && (last try success ¦¦ long from last failure) && want to turn right
S5 | no collision && wait too long
S6 | no collision && wait too long
S7 | no collision && the left GAP is suitable
S8 | no collision && the right GAP is suitable
S9 | no collision && ego Car run in the target lane
S10 | no collision && ego Car run in the target lane
S11, S12, S13, S14, S15, S19 | there is a collision
S16 | no collision
S17 | no collision && want to change left
S18 | no collision && want to change right

## Slide 31: Back-up
Deceleration in FSRA (Full Speed Range ACC)
Source: Prof. Dr. rer. Winner, MAA SS2019 Script,
Chapter 4.1 Adaptive Cruise Control, page 13

## Slide 32: Back-up
Interaction with ahead obstacles
  : comfort braking distance
  : FSM update driving distance
  : minimal braking distance at low-speed condition
  : coordinate offset (baseline offset)

## Slide 33: Back-up
Communication with traffic lights

## Slide 34: Back-up
Communication with traffic lights
  : comfort braking distance
  : emergency braking distance
  : emergency braking distance weight
  : FSM update driving distance
  : minimal braking distance at low-speed condition

## Slide 35: Back-up
Determination of motion target

## Slide 36: Trajectory planning
Motion control
  P control on steering angle
      Cumulative error due to finite difference calculation in inverse Frenet transformation
  Lateral offset dominated control
      Middle lateral distance  large turning radius
      Large lateral distance  small turning radius
symbol | value
 | 8
N | 5
 | 0.1
 | 0.25
 | 0.2
 | 80 m
 | 20 m
 | 0.2 m
 | 0.3 m
symbol | value
 | 8
N | 5
 | 0.1
 | 0.25
 | 0.2
 | 80 m
 | 20 m
 | 0.2 m
 | 0.3 m

## Slide 37: Back-up
Open loop test
  overtaking judgement (other state -> Prep Change lane left)
TTC1
  TTC1: time to the front obstacle
  TPCL: time to Prep Change Lane Left

## Slide 38: Behavior Planner – (Straight FSM)
1. Ensure body length
2. Avoid collision
y
x
obstacle
ego car
obstacle